TERMSERV 1.1 - an example terminal server
Copyright (c) 1990, 1999 Erick Engelke

TERMSERV.EXE (in binary form) is distributed freely in the hope that it
may prove interesting or useful, but with no warrantee of any kind.

Purpose
=======
    Termserv allows incoming TELNET sessions direct access to serial
    ports in the local machine.

    So one might hook up four modems and use this to TELNET to the modem
    pool.  Or one may connect to the serial line of a network switch
    and use this program to access the switch's console.

    This program also includes an FTP server and a Web server, including
    real-time generation of a usage graph.

    Finally, this program will optionally Email to a specified Email address
    each time it is restarted, and SYSLOG entries on restart, and as each
    connection arrives and later departs.

Configuration
=============
    Edit the TCP.CFG file and set the following parameters:

  [settings]
    ip=x.x.x.x              dotted IP address of this station, or BOOTP
    netmask=255.255.255.0   or whatever is the appropriate network mask
    gateway=x.x.x.x         dotted IP address of the router

    nameserver=x.x.x.x      dotted IP address of the name server
    smtp.gateway=x.x.x.x    dotted IP address of an Email relay host
    smtp.hostname=blah.blah DNS name for this machine, required by
                            many SMTP servers, must be set correctly

    ftpd.password = "frog"  any case sensitive password for your FTP service
    email.notify = "erick@ertos.com"  the Email address of recipient

    syslog.host = x.x.x.x   option host to receive our syslog information

    userid=joe              userid/password for web access
    password=blow

  [com1]                    repeat this section for com1 through com4
    speed=9600
    irq=4

Programming
===========
    This is a multithreaded program using the commercial eRTOS development
    system.  eRTOS is great for developing embedded network and/or serial
    applications - this program demonostrates both network and serial i/o
    and is actually one of the example projects.

    This entire program took less than three hours to write.  The non-web
    part is two printed pages of C, and the web part (including graphics)
    is another two pages.  eRTOS includes code to do graphics, and charts.

    For more information about eRTOS, see http://www.ertos.com